750 Giulietta Series are commonly identified on the right side of the firewall in the engine bay. The number will start with usually 1493.xxxxx for Sprint and Sprint Veloce's, 1495.xxxxx for Spiders and Spider Veloce's, 1468.xxxxx for the Berlina TI, and regular Berlina's start with 1488.xxxxx. Below is a list of the serial number provided by Alfa Romeo in previously printed texts.

Sprint & Berlina

1493.00011-00023 = 1954	                     1488.00002-01431 = 1955

1493.00024-01438 = 1955	                     1488.01432-07780 = 1956

1493.01439-03545 = 1956                      1488.07781-16720 = 1957

1493.03546-06008 = 1957                      1488.16721-22492 = 1958

1493.06009-07921 = 1958	                     1488.22493-24931 = 1959

1493.07922-10301 = 1959	                     1488.31993-35200 = 1960

Sprint Veloce & Berlina TI

1493.01439-03545 = 1956	                     1468.00027-01295 = 1957

1493.03546-06008 = 1957	                     1468.01296-11243 = 1958

1493.06009-07921 = 1958	                     1468.11244-17760 = 1959

1493.07922-10301 = 1959	                     1468.24011-34200 = 1960

Spider

1495.00016-00017 = 1955

1495.00018-01039 = 1956

1495.01040-03232 = 1957

1495.03233-05619 = 1958

1495.05620-07213 = 1959

Spider Veloce

1495.00018-01039 = 1956 Only 18 were made

1495.01040-06008 = 1957 Only 32 were made

1495.03233-05619 = 1958  835 were made

1495.05620-07213 = 1959  368 were made

Note: Sprint and Spider, and Veloce model of either, serial numbers were interspersed with the Normale's. Part of this was due to Homologation for racing purposes and the other was just bad bookeeping to some extent. If you have what you believe is a Sprint or Spider Veloce, it would have to be within these number series for that given year. A secondary point of identification will in the same spot as the body placard, either above or below, and will start with a 750X. The "X" will have a letter designation as listed below.

B = sprint

C = berlina

D = spider

E = sprint veloce

F = spider veloce

In addition to all that, a third place to confirm engine identification for the specific vehicle would be by the hood support strut of the Spider or Sprint models. On Berlina models this can be located on the Passenger side fender well area. For identifying you 1955 to 1959 1300cc engine, look by the distributor for the engine number.

Engine#					Model

1315.00.001 - 09.002			750B Sprint

1315.50.001 - 74.950			750C Berlina

1315.40.001 - 45.854			750D Spider

1315.30.001 - 33.000			750E Sprint Veloce

1315.30.001 - 33.000			750F Spider Veloce

Note: To add to the confusion new engines that were replaced by the factory through authorized mechanics and shops, during the early years, often arrived without serial numbers. The shops or mechanics were supposed to imprint the serial number of the old engine on the new one, which may or may not have been done.

Compiled and Researched by Jim Allen and Steve Richards.